Yough Cougar Rocketry Team

Project Dorothy

Table of Contents

Summary of FRR Report 		2

Launch Vehicle and Payload Summary 		3

Changes made since CDR 		3

Vehicle Criteria 		4

Proper Use of Materials 		4 – 13

Previous Analysis to Improve Design 		14

Suitability of Fin Shape 		14

Workmanship and Mission Success 		15

Safety and Failure Analysis – Launch Vehicle 		15 – 16

Recovery Subsystem 		17 – 18

Safety and Failure Analysis – Recovery Subsystem 		18 – 19

Mission Performance Predictions		20 – 28

Safety and Environment (Vehicle)		29 – 30

Payload Integration		31

Payload Criteria		32

Science Value		33

Experiment Design of Payload		35 – 37

Flight Performance Predictions and Possible Graphical Scenarios		38 – 41

Safety and Environment for Payload		47 – 50

Launch Operations Procedures		51 – 55

Safety and Quality Assurance		56 – 59

Activity Plan		60

Budget  Plan 		60 – 63

Timeline 		64 – 67

Outreach 		68 – 72

Conclusion 		73

I).	 Summary of FRR Report

“Project Dorothy”

Yough High School Rocketry Team

919 Lowber Road

Herminie, PA 15637

724 – 446 – 5520 ext. 2015

Student Participants

- Bickerstaff, Amy – YHS Senior, Vehicle Design, Team Lead, and Schedule Manager

- Wiley, Ashley – YHS Junior, NAR & FAA Regulations and Flight Control, Payload

- Abbott, Stephanie – YHS Sophomore, Safety Operations Manager

- Sarosinski, Josh – YHS Sophomore, Hazardous Materials and Environmental Concerns

- Bowser, Alicia – YHS Senior, Assistant – Not participating in the trip to Huntsville

Administrative Staff Members

- Donald L. Gilbert, Jr. – Physics and Gifted Teacher, TARC coordinator

  - Phone: (724) 446 – 5520 ext. 2015

  - Email: gilbertd@yough.k12.pa.us

Main NAR, TRIPOLI and Other Field Specific Mentors

- Ernest Walters – TRIPOLI Pittsburgh – Level 3 Certified

  - Uniontown, PA

  - Phone: (724) 439 – 9062

- Eric Haberman – TRIPOLI Pittsburgh – Westinghouse Corporation

  - West Newton, PA

  - Phone: (412) 337 – 5799

- Joe Pscolka – TRIPOLI Pittsburgh – Level 3 Certified

  - Washington, PA

  - Phone: (724) 945 – 6605

Launch Vehicle Summary

- Four Inch fiberglass airframe, 124 inches in length, approximately 530 ounces in mass

- Animal Motor Works L900RR motor to be used

- Dual deployment, dual altimeter with two ejection charges, 18 inch drogue, SkyAngle CERT-3 Large main chute

- 1 ½ inch rail size to be used

Payload Summary

- Crepe paper wrapped paint balls to mimic maple tree seed pods for dispersion

- Electronic data logger with temperature, and relative humidity sensors

II).	Changes made since CDR

Changes to Vehicle Criteria

Based on the proposed weight of the launch vehicle, RockSIM analysis indicates that the Animal Motor Works L900RR would be most appropriate for the application.  The SkyAngle Classic 60 parachute has been replaced with a SkyAngle CERT-3 Large parachute due to the increased mass of Dorothy.

Changes made to Payload Criteria

A sabot ejection system will be utilized to expend the whirly birds, data logger, and main parachute. Testing with the sabot ejection system has been successful with a few minor issues still being addressed. Two data loggers have been acquired for temperature and relative humidity analysis. One will be a ground station taking samples every 10 seconds; the other will be released with the whirly birds during the main ejection phase with a sample rate of one reading per second.

Changes made to the Activity Plan

The outreach has been modified due to the team being unable to work with the middle school students.  Outreach will now be held in the community with Starhawk rockets being given to children.  A rocket fair will be held on March 29, 2008 regardless of the weather conditions.  Seventy-five Starhawk rockets were distributed during the fundraising events held at Sam’s Club on February 2 and at Giant Eagle on February 10, 2008.  These sales accumulated approximately $700 toward expenses for the rocketry team.

III).	Vehicle Criteria

Proper Use of Materials

For the main airframe, the team has selected four-inch fiberglass G12 tubing. The group chose the four-inch fiberglass tubing because of its functional ability to easily retain the payload and it’s structural rigidity. Bulk plates for the electronics bay are cut from ¼ inch G10 fiberglass to ensure a quality mounting point for the U-bolts which are attached to stainless steel braided wire.  This wire is then attached to the engine mount in the aft section of the airframe.  Kevlar chord attaches the forward compartment with the whirly birds and main parachute.  All the fastening hardware selected is of stainless steel materials so that the structural integrity is maximized and the probability of stress fractures is minimized.  Ball bearing swivel clips attach to any area where entanglement is not desired.  The fins area a through the wall design, constructed of .1875-inch (3/16 inch) G-10 fiberglass. G-10 fiberglass was highly recommended by many of the TRIPOLI high power rocketry members, therefore being an obvious choice for this project due to its high tensile strength and breaking resistance. To ensure proper assembly, local high power rocket mentors, Ernie Walters, Eric Haberman, and Joe Pscolka, will be overseeing the complete building process. Having this supervision enables the team to design, construct and test the rocket and its components properly.

Assembly of Dorothy II begins with three fin slots being cut into one section of the 48-inch fiberglass tubing.  The motor mount, constructed of a 75-millimeter fiberglass tube, with three G10 centering rings will be inserted and epoxied into the main airframe.  Before the epoxy sets, the fins are inserted into the slots where they will lock into the centering rings of the motor mount.  Epoxy will then be injected into the slots so that the epoxy will be in contact with the motor mount and the interior of the airframe.  Once these parts fit properly, a jig designed to hold the fins in a perfect 120-degree alignment will be placed onto the airframe.  A final bead of epoxy will then be placed along the fin and airframe exterior.  Once the epoxy has dried, a thin layer of PC-7 will be used to smooth the surface between the airframe and the fins to reduce wind resistance as well as improve the appearance of the launch vehicle.

CADD drawings created by Eric Haberman show the Center of Pressure and Center of Gravity as well as locations for vent holes and linear dimensions.

The assembly can be seen in multiple sections with the components in view.

The assembled Dorothy II with the internal parts shown.

Motor Mount Retention

Eric Haberman has designed a custom built motor mount for application into Dorothy II.  This design allows for both Aerotech and Animal Motor Works systems to be used easily due to a snap ring configuration that prevents the motor from exiting the mount without complete removal of the snap ring.   Various adapters have been constructed to accommodate motor case lengths and enclosure features.  Members of the TRIPLOI Pittsburgh rocketry group have used this design for many years with very high success rates.  At this time, no failure has ever been reported back to Mr. Haberman.

Assembly Process of Sustainer

Upon completion of the motor mount, fins, and lower airframe, assembly of the sustainer began.  The motor mount was inserted into the airframe partially in order to clear the second centering ring.  Each fin was inserted into the slot made through the airframe.

Note that the edges of the fins were roughened to allow the epoxy to have a surface to grab rather than the smooth surface where little adhesion would take place.

The rear of each fin has a small notch cut into it to allow for the third centering ring to provide a positive lock.  This prevents the fin from slipping out of the airframe even if the epoxy were to fail.  By extending the fins leading edge into the airframe, the fin cannot dismount without shearing of the G10 fiberglass.  All of these safety features were taken into account after careful analysis of the fin separation in the 2007 SLI crash of Dorothy I.

Here the fins are shown locked into the rear centering ring.  Notice the rough groove in line with the location of where the airframe tube will meet.  The epoxy will adhere to the surface very well providing a secure bond.

This close-up view of the motor mount shows how the fins lock into the aft centering ring for a positive connection.

With the fins inserted into the airframe and locked into position, the Loctite HP-20E Hysol epoxy is injected into the airframe so that epoxy joins the fins to the motor mount.  Then epoxy is used to form a bead along the edge of the airframe and fins where the rough grindings were created to allow a strong bond.  Not shown is the jig made to hold the fins in a perfect 120-degree position.

To allow for better airflow, PC-7 is applied to the airframe and fins to smooth the epoxy bead and achieve a higher level of appearance as well as functionality.

# Previous Analysis to Improve Design

The flight characteristics of Dorothy I from SLI 2007 showed that even in moderate to high wind condition ( 15- 30 mph ), the launch vehicle was able to maintain a nearly vertical flight.  Design improvements for SLI 2008 included the sabot ejection system for the 800-foot deployment, glow plug ignition for powder charges, and the ability to place mass in the nosecone to adjust the center of gravity slightly.

Suitability of Fin Shape

The fin shape of Dorothy II is very suitable for this particular mission.  Due to the length of Dorothy II, fins of a large surface area are not required since the center of gravity is many calibers forward of the center of pressure. Multiple fin shapes were attempted using Rocksim and none seemed to be as aesthetically pleasing while maintaining the desired CP.  The use of three fins also helps Dorothy II to resist weather cocking due to the wind and fly vertically.  This is especially useful for the mission since the objective of Dorothy II is to fly a mile high in the air, where wind speeds can reach higher levels.

Workmanship and Mission Success

A launch vehicle of this size must be constructed carefully in order to prevent or eliminate malfunctions of the systems vital to safe recovery.  Proper cutting of materials to provide smooth edges and uniform dimensions are a necessity during this process.  Eric Haberman utilizes precise cutting instruments both at his home and at the Westinghouse facility to ensure that all materials are finished in the same manner and alignments are precise.  All epoxy joints are smoothed to allow for proper airflow and reduce drag, which could cause yawing of the vehicle.  Even spacing of the fasteners is taken into account so that rotational failures do not occur.  Smoothing of the airframe prior to painting is also carefully administered so drag is reduced and a mirror perfect finish can be applied.  This not only provides for an aesthetically pleasing design, but also quite functional.

# Safety and Failure Analysis – Launch Vehicle

| Failure Modes | Causes | Effects | Restrictive Mitigations |
| --- | --- | --- | --- |
| Dismount of Fins | Improper attachment of fin to airframe | Fins detach and fall/flutter to the Earth uncontrollably Launch Vehicle begins unsafe trajectory | Proper attachment of fins to the airframe and visual inspection of epoxy cracks |
| Engine Misfire | Faulty Motor Faulty Igniters Improper Preparation | The rocket may not leave the launch pad at a safe velocity Engine may not burn entirely | Proper Inspection of igniters Inspection of proper motor assembly |
| Engine Dismount | Improper installation of motor retaining system | Engine could slide out of Airframe and free fall to the ground causing injury Rocket may not reach desired altitude or yaw in an unsafe direction Engine may propel itself toward the ground and possibly spectators KATO | Proper installation of engine retaining system and multiple inspections of the retaining device |

Safety and Failure Analysis – Launch Vehicle Continued

| Engine Detonation | Defective engine from factory | Motor self destructs, and launch vehicle destruction KATO | Inspect motor grain pellets during installation into reloadable motor system |
| --- | --- | --- | --- |
| Premature Ignition | Accidental ignition from igniter or static electricity | Vehicle lift off before desired Onboard electronic devices not enabled causing possible recovery failures | Proper safety switches Static Free Environment |
| Parachute not deploying | Deployment charge not igniting Payload absorbing energy from the ejection charge | Unsafe Landing | Bench test and Redundant System Designs Sabot style ejection system |
| Electronics bay malfunction | Loss of power to electronics Faulty electronics | Ejection not occurring | Bench test and Redundant System Designs |
| Parachute Detachment | Malfunction of shock cords, cables, or attachment points | Parachute and rocket separation occurring and possibly a dangerous landing situation | Inspect all parts for damage before installation Replace as needed |
| Shear pins not shearing | Not enough pressure applied from ejection charge | Parachute not deploying and possible crash landing | Bench test and analyze |

Recovery Subsystem

According to the data provided by RockSIM, the suitable parachute size for Dorothy II is a SkyAngle CERT-3 Large.  The attachment scheme of Dorothy II’s recovery subsystem is a 3/16 inch Kevlar chord attached to a ball bearing swivel clip which are attached to a 1/8 inch braided stainless steel cable.  The G-Wiz LC800 Deluxe altimeters at an above ground altitude of approximately 1000 – 800 feet, perform deployment of the main parachute.  One altimeter fires a glow plug contained in an aluminum pyrowell holding 1.5 grams of 4Fg black powder.  Altimeter number two will use an e-match inserted into the same pyrowell.  The pressure generated by this charge pushes a piston up the airframe into the sabot containing the whirly birds and main parachute.  The fiberglass sabot then impacts the nosecone, breaking the shear pins allowing the sabot to exit the airframe and release the contents.  The sabot pieces are attached to stainless steel braided cables so that the pieces do not fall to the earth uncontrollably.

Test results of this system have been quite successful.  Early tests resulted in the bulkhead of the piston separating from the piston body.  The solution to this problem was to create an aluminum piston to replace the fiberglass piece.   It was also noted that the short lengths of cable to secure the sabot sides were too short, resulting in the detachment of the retaining device from the fiberglass sabot.  Lengthening of the cables allowed the sabots pieces to travel further and slow down sufficiently so that excessive forces were not encountered, thus retaining the pieces.

Deployment Process:  Gunpowder Equations

PSI by Airframe Diameter and Desired Force Airframe

Diameter 	100 Pounds 	150 Pounds 	200 Pounds 	250 Pounds

2.6" 	              19 psi 	   28 psi 	      38 psi 	     47 psi

4.0" 		    8 psi 	   12 psi 	      16 psi 	     20 psi

6.0" 		 3.5 psi 	  5.3 psi 	     7.0 psi 	    8.8 psi

7.5" 		 2.3 psi 	  3.4 psi 	     4.5 psi 	    5.7 psi

The table shows that smaller diameter airframes may need a higher pressure than larger diameter airframes.

Once you've selected a desired force (150, 200 or 250 pounds) on the nose cone, determine the psi that will produce that force. For example, 16 psi will put 200 pounds of force on the nose cone of a 4" diameter rocket.

To determine the amount of black powder (BP) to produce the desired pressure, use the equation as shown below.

C * D * D * L = grams of BP

* C - one of the values listed below

0.002 = 5 psi

0.004 = 10 psi

0.006 = 15 psi

0.0072 = 18 psi

0.008 = 20 psi

* D = airframe diameter, in inches

* L = length of the cavity to be pressurized, in inches

The Yough Cougar Rocketry team has calculated that Dorothy II will require less than 1.0 grams of black powder to successfully eject the parachute and payload.  However, to unsure airframe separation, 1.5 to 2.0 grams of 4Fg black powder will be used.  Testing with this amount of powder worked quite successfully and did not result in any damage to the airframe or internal parts.

Safety and Failure Analysis – Recovery Subsystem

| Failure Modes | Causes | Effects | Restrictive Mitigations |
| --- | --- | --- | --- |
| Parachute not deploying | Deployment charge not igniting Payload absorbing energy from the ejection charge | Unsafe Landing | Bench test and Redundant System Designs Sabot style ejection system |
| Electronics bay malfunction | Loss of power to electronics Faulty electronics | Ejection not occurring | Bench test and Redundant System Designs |
| Parachute Detachment | Malfunction of shock cords, cables, or attachment points | Parachute and rocket separation occurring and possibly a dangerous landing situation | Inspect all parts for damage before installation Replace as needed |
| Shear pins not shearing | Not enough pressure applied from ejection charge | Parachute not deploying and possible crash landing | Bench test and analyze |

Safety and Failure Analysis - Recovery

In order to prevent a recovery subsystem failure, the following safety precautions will be followed:

Before the rocket launches

- Arm the ejection charge systems, have safety member verify LCX altimeter ready beeps

- Ensure that personnel do not drop or damage the launch vehicle which could cause system failures

To mitigate such things from happening

- Have more than one person overlooking preparation of recovery subsystem armament

- Make sure that everyone is in the safety zone before activating recovery altimeters

- All personnel need to be aware of the surroundings and safety zones

- Store rocket in a secure location away from travel areas

During the rocket launch

- Personnel could lose visual contact with the launch vehicle

- Rocket could have a malfunction resulting in pieces falling dangerously and striking someone

To mitigate such things from happening

- Have more than one person watching the rocket and pin-pointing a location for landing

- Watch the rocket at all times and if debris or shrapnel flies, get to a safe zone with cover

- Keep and eye on where any debris has landed in order to recover and pick up to prevent environmental harm

Mission Performance Predictions

The mission of “Project Dorothy” is to construct a launch vehicle containing a scientific payload that will achieve an above ground level altitude of 5280 feet (one mile) and safely deploy the payload as well as return to ground level to be reused.

The requirements of the launch vehicle are to liftoff from the launch pad without yawing drastically in any wind conditions to ensure nearly vertical flight characteristics with a motor of sufficient thrust to achieve the above ground level altitude of one mile while the G-Wiz LC 800 altimeters fire the drogue parachute charge upon apogee and the main charge at 800 feet above ground level to ensure safe descent rates in order to minimize or prevent any damage to the launch vehicle.

Success of the launch vehicle mission will be to analyze the altimeter data to verify the above ground level altitude from each of the G-Wiz LC 800 altimeters (2), monitor visually the successful deployment of the drogue and main parachutes at the desired altitudes as well as the firing of the ejection charges, and inspect the launch vehicle for damage upon retrieval to the earths surface.

Dorothy II is designed using the same data from her big sister Dorothy I from SLI 2007.  The extreme length of the launch vehicle is to ensure more than adequate stability characteristics.  Testing of smaller scale rockets, even on low thrust motors showed nearly no yaw (weather cocking) even in moderate to high wind conditions.  The through the wall fin design ensures that the fins will remain in the structure during the entire range of the flight.  Fiberglass tubing was selected for its lightweight and low cost, as well as workability with hand tools and small power equipment.  The G-Wiz LC 800 was selected as the altimeter due to its ease of use and dual deployment features on multiple batteries.  SkyAngle parachutes were chosen due to their proven reliability at other high power rocketry events.  The sizes were determined after discussion with level II and level III Tripoli members.

Altitude Prediction – RockSIM

According to the data provided by RockSIM for the Dorothy II launch vehicle, an above ground altitude of 5617 feet will be achieved.  In previous practice with RockSIM, it was noted that a -10% margin of error was common, thus resulting in a possible altitude of anywhere between 5055 feet to the 5617 feet prediction.

Component Weights for Dorothy II

The component weights for Dorothy II were measured and entered into RockSIM before assembly.  Additional weight was added to the launch vehicle to account for the epoxy, PC-7 and paint applied to the vehicle.  A measurement of Dorothy II using a bathroom scale shows that the vehicle weighs 21 pounds without paint applied.  The RockSIM estimate of 25 pounds without the motor loaded will be very close to the actual weight once paint is applied.  Therefore, the team believes that the flight simulation data provided by the RockSIM will yield excellent results.  This reaffirms that the selection of the Animal Motor Works L900RR was the correct choice.

# Comparison of mathematical values versus actual

According to the RockSIM program, the Center of Gravity is located 69.8220 inches from the nose of the launch vehicle.  A simple, yet effective test was to place a broom handle under the airframe while members of the team slid the airframe forward and back until the rocket was balanced on the broom.  This test agreed with the RockSIM data to within ½ inch once again verifying the team’s beliefs in the data provided by RockSIM.

Thrust Analysis of Animal Motor Works L900RR

Thrust for the Animal Motor Works L900RR for the launch vehicle is provided in less than four seconds.  The graph shows this burn time only and does not include the coasting or recovery phases.  The L900RR was selected due to a slightly smoother thrust curve rather than the sharp spike from the L1150.  This was to minimize stress on the internal components while still achieve the desired above ground level altitude.

Rocksim analysis of Dorothy II

Locations for the Center of Pressure and Center of Gravity for Dorothy II were found using Rocksim.  During the construction, component weights were adjusted using the mass override feature so that variations were noted.  During this process, most of the calculated masses by Rocksim were very close to the actual measured values, thus proving that the data in Rocksim was quite accurate.  The two-dimensional drawing from Rocksim is provided below.

Simulation results for Dorothy II

Engine selection

[L900RR-None]

# Simulation control parameters

- Flight resolution: 800.000000 samples/second

- Descent resolution: 1.000000 samples/second

- Method: Explicit Euler

- End the simulation when the rocket reaches the ground.

# Launch conditions

- Altitude: 0.00000 Ft.

- Relative humidity: 50.000 %

- Temperature: 59.000 Deg. F

- Pressure: 29.9139 In.

Wind speed model: Breezy (15-25 MPH)

- Low wind speed: 15.0000 MPH

- High wind speed: 25.0000 MPH

Wind turbulence: Fairly constant speed (0.01)

- Frequency: 0.010000 rad/second

- Wind starts at altitude: 0.00000 Ft.

- Launch guide angle: 0.000 Degrees from vertical

- Latitude: 0.000 Degrees

Launch guide data:

- Launch guide length: 120.0000 In.

- Velocity at launch guide departure: 51.524 ft/s

- The launch guide was cleared at : 0.251 Seconds

- User specified minimum velocity for stable flight: 43.9993 ft/s

- Minimum velocity for stable flight reached at: 90.3595 In.

Max data values:

- Maximum acceleration:Vertical (y): 471.418 Ft./s/sHorizontal (x): 7.432 Ft./s/sMagnitude: 471.419 Ft./s/s

- Maximum velocity:Vertical (y): 624.1479 ft/s, Horizontal (x): 24.9221 ft/s, Magnitude: 640.0424 ft/s

- Maximum range from launch site: 1775.18966 Ft.

- Maximum altitude: 5374.44574 Ft.

# Recovery system data

- P: Main Parachute Deployed at : 69.724 Seconds

- Velocity at deployment: 94.3237 ft/s

- Altitude at deployment: 799.90546 Ft.

- Range at deployment: -633.87803 Ft.

- P: Drogue Parachute Deployed at : 18.928 Seconds

- Velocity at deployment: 99.1190 ft/s

- Altitude at deployment: 5374.44571 Ft.

- Range at deployment: -1775.18966 Ft.

Time data

- Time to burnout: 3.790 Sec.

- Time to apogee: 18.928 Sec.

- Optimal ejection delay: 15.138 Sec.

# Landing data

- Successful landing

- Time to landing: 103.934 Sec.

- Range at landing: 187.68887

- Velocity at landing: Vertical: -22.8149 ft/s , Horizontal: 24.9222 ft/s , Magnitude: 33.7881 ft/s

# Competition settings

Competition conditions are not in use for this simulation.

# Safety and Failure Analysis – Mission Performance

| Failure Modes | Causes | Effects | Restrictive Mitigations |
| --- | --- | --- | --- |
| Dismount of Fins | Improper attachment of fin to airframe | Fins detach and fall/flutter to the Earth uncontrollably Launch Vehicle begins unsafe trajectory | Proper attachment of fins to the airframe and visual inspection of epoxy cracks |
| Engine Misfire | Faulty Motor Faulty Igniters Improper Preparation | The rocket may not leave the launch pad at a safe velocity Engine may not burn entirely | Proper Inspection of igniters Inspection of proper motor assembly |
| Engine Dismount | Improper installation of motor retaining system | Engine could slide out of Airframe and free fall to the ground causing injury Rocket may not reach desired altitude or yaw in an unsafe direction Engine may propel itself toward the ground and possibly spectators KATO | Proper installation of engine retaining system and multiple inspections of the retaining device |
| Engine Detonation | Defective engine from factory | Motor self destructs, and launch vehicle destruction KATO | Inspect motor grain pellets during installation into reloadable motor system |
| Premature Ignition | Accidental ignition from igniter or static electricity | Vehicle lift off before desired Onboard electronic devices not enabled causing possible recovery failures | Proper safety switches Static Free Environment |

Safety and Failure Analysis – Mission Performance Continued

| Parachute not deploying | Deployment charge not igniting Payload absorbing energy from the ejection charge | Unsafe Landing | Bench test and Redundant System Designs Sabot style ejection system |
| --- | --- | --- | --- |
| Electronics bay malfunction | Loss of power to electronics Faulty electronics | Ejection not occurring | Bench test and Redundant System Designs |
| Parachute Detachment | Malfunction of shock cords, cables, or attachment points | Parachute and rocket separation occurring and possibly a dangerous landing situation | Inspect all parts for damage before installation Replace as needed |
| Shear pins not shearing | Not enough pressure applied from ejection charge | Parachute not deploying and possible crash landing | Bench test and analyze |
| Parachute not deploying | Deployment charge not igniting Payload absorbing energy from the ejection charge | Unsafe Landing | Bench test and Redundant System Designs Sabot style ejection system |
| Electronics bay malfunction | Loss of power to electronics Faulty electronics | Ejection not occurring | Bench test and Redundant System Designs |
| Parachute Detachment | Malfunction of shock cords, cables, or attachment points | Parachute and rocket separation occurring and possibly a dangerous landing situation | Inspect all parts for damage before installation Replace as needed |
| Shear pins not shearing | Not enough pressure applied from ejection charge | Parachute not deploying and possible crash landing | Bench test and analyze |

Safety and Environment ( Vehicle )

Stephanie Abbott is the Safety Officer for the Yough Cougar Rocketry Team.

Failure of the following launch vehicle items must be addressed to ensure safe flight and recovery of Dorothy II.

Fins: In the event that a rocket fin would fall off, then the rocket could possibly fly uncontrollably in any direction.  To prevent such an event, ensure that the fins are properly epoxied into the airframe and that the fin material is of appropriate strength to withstand the forces encountered.  Attachment of the fins is via a through the wall design with a locking tab on the fin securing it to the third centering ring on the motor mount.  A complete failure of the G10 fiberglass must happen in order to have fin detachment.

Motor: In the event that the motor doesn’t fire properly,

- the motor may not have enough thrust causing the vehicle to not reach its potential apogee

- vehicle may not leave the rail with sufficient velocity causing it to follow a horizontal path

- incomplete motor burn or thrust deviation may result in false triggering of the ejection system

Payload Integration: All the whirly birds and Toto must be placed in the sabot as to not interfere with the recovery system.  The main payload section will be packed as follows from nose to tail.  Nosecone, Kevlar shock cord, SkyAngle CERT-3 Large Parachute, Kevlar shock cord passing through Toto and the whirly birds attaching to the piston.  The sabot surrounds the parachute and whirly birds and is secured to the piston with braided stainless steel cables.  The parachute is placed at the top of the system to catch air quickly and assist in drawing the payload out if the piston does not reach its full displacement.  In order to minimize malfunctions, place the whirly birds as far aft as possible in the sabot.  If excess room is present between the parachute and whirly birds, insert wadding in order to minimize payload shifting.

Recovery System: In the event that the recovery system does not deploy, the launch vehicle could descend to earth in a ballistic style, which may cause serious injury to bystanders.  To prevent this occurrence, several system tests on the ejection system have been and will continue to be performed.

Personal Hazards and Avoidance Procedures

Fiberglass in the eyes: wear safety goggles

Sawdust in the eyes: wear safety goggles

Cuts from fiberglass or sharp instruments: wear safety gloves and body protectors to cover and protect any area where skin shows

Headaches from fumes of paint: wear a breathing mask to cover the mouth and face to prevent inhalation of fumes, and to also paint in well ventilated area, such as a paint booth

Refer to MSDS sheets from the manufacture for special instructions

Tripping over wires: tape wires down to the ground, and if falling does occur, check for cuts and bruises to be bandaged if necessary. Sanitize all the affected areas with materials from First Aid Kit.

Other First Aid: Be sure to locate first aid kit in a location convenient to all personnel in the working environment in case injury occurs

Ensure that regulations and procedures required by the NAR are observed at all times.  Instructions for all internal devices and deployment systems are to be kept in a binder as well as any MSDS sheets for materials being handled.

Environmental Concerns ( Launch Vehicle )

If the rocket catches on fire then

- Wild-fire can occur if grass is dry enough

- Scorching of area around rocket can occur if grass is a little wet

- Items that fall off the rocket and are not recovered due to loss of visual tracking or paying attention could possibly be digested by animals causing illness

Things to do to prevent such things from happening

- Spray the launch area with water prior to launch

- Have multiple personnel track the vehicle and payload to monitor any loose parts

# ( Payload )

The whirly birds are constructed of crepe paper and paint balls, both of which are biodegradable.  These pose little to no risk to the environment.  The data logger is constructed of hard plastic and includes a lithium battery.  Recovery of this device is essential to mitigate environmental situations.  A designated spotter will track this device specifically.  A parachute of a high contrast color will be attached to this device so that it is easy to spot both in the air as well as on the ground.

Payload Integration

All the whirly birds and Toto must be placed in the sabot as to not interfere with the recovery system.  The main payload section will be packed as follows from nose to tail.  Nosecone, Kevlar shock cord, SkyAngle CERT-3 Large Parachute, Kevlar shock cord passing through Toto and the whirly birds attaching to the piston.  The sabot surrounds the parachute and whirly birds and is secured to the piston with braided stainless steel cables.  The parachute is placed at the top of the system to catch air quickly and assist in drawing the payload out if the piston does not reach its full displacement.  In order to minimize malfunctions, place the whirly birds as far aft as possible in the sabot.  If excess room is present between the parachute and whirly birds, insert wadding in order to minimize payload shifting.

The fiberglass sabot is compatible with the fiberglass airframe perfectly.  Performance Rocketry manufactured all the fiberglass components to the same tolerances.  The sabot is actually a piece of fiberglass coupler cut in half.  Since some of the material is now missing from the coupler, the fit provides an easily movable section, yet long enough and of proper diameter to prevent binding during ejection.  The parachute, Toto, and whirly birds slide easily in the polished coupler with ease.  The payload housing is the sabot itself.  These fiberglass units are very strong and crush resistance.  During ejection, the piston slams into the sabot forcing it into the nosecone shearing the pins.  The sabot encounters a great deal of force, therefore making fiberglass the best choice for the design.

Pictured above is the payload sections and main parachute deployment systems. The electronics bay houses the Perfectflite LCX flight computers with glow plug ignition pyrowells. The aluminum piston slides easily through the upper sustainer tube and is attached with a stainless steel cable. Additional cables attach the sabot halves. A Kevlar shock cord (not shown) attaches to the piston, through the swivel clip on the SkyAngle parachute and finally to the nose cone.

IV) Payload Criteria

Experiment Concept

The whirly bird part of the scientific payload uses objects that are found in any consumer retail store. The whirly birds are made up of crepe paper and a paintball. Toto, the mechanical whirly bird, is composed of electronic sensors, electronic download devices, and computer hardware, which analyze data from the current weather conditions.  Such hardware and assembly is not available in a “off the shelf” environment and must be purchased and assembled by a knowledgeable person.  Originally the design was to release confetti during the recovery segment of the flight.  However, this would have proven quite difficult to track each piece of material and/or recover to mitigate environmental harm.  Upon further review, programs used by weather gathering researchers conducted similar studies, but on a much more complicated level.  Here the goal was to simplify the study to make the data more available for anyone to study and interpret.

The whirly bird is itself a very unique item that attempts to imitate a common natural phenomenon, the procreation of a maple tree.  Many Americans can identify with the fluttering of a maple tree seedpod from their own backyard.  Who in their right mind would consider placing a man made version of this natural occurrence?  To answer that, you need not look any further than the entangled mind of our team leader, Miss Amy Bickerstaff.  The significance of placing the whirly birds and Toto in a secure pouch enables our team to study the variations of wind patterns and current weather conditions given on the day of flight.

The suitable level for Amy Bickerstaff, Alicia Bowser, and Ashley Wiley are medium in the challenge level, because this is their third year in rocketry, and second year for a returning team in SLI. Josh Sarosinski and Stephanie Abbott are attempting a medium high challenge level, because they are second year rocketry members and only first year SLI members.  The main challenge for all the members is to take a complex project and simplify it so that anyone can understand its value.  Another issue for the team has been in trying to understand all of the complicated details to writing the Proposal, PDR, CDR, and FRR based on guidelines that seem to duplicate themselves and at times make little to no sense.

Science Value

The objective for the scientific payload is to determine if the predicted values for the dispersal of the whirly birds based on surface level winds is accurate with the actual dispersal after ejection from the launch vehicle.

The mission will be to recover and mark 75% of the pods for the splatter gram.  The payload deployed with the main parachute will release 100 whirlybird pods. The payload data will then be analyzed using statistical methods to compare the theoretical data before flight and the actual results.  During ejection of the drogue parachute, a large amount of colored chalk dust will be deployed from the parachute protector.  This is to mark the location of the apogee deployment and better track the launch vehicle.  No scientific data analysis will be done on this substance.  It is solely for tracking purposes, as the dust cloud will travel a distance outside of the launch area.

Another payload item that the Cougar Rocketry Team will include in Dorothy II will be an electronic whirly bird to mimic the ones that were used in the movie “Twister.”  Obviously the movie made data pods seemed to gather a large amount of information very quickly.  The data logger that the team is using will include a temperature and relative humidity sensor.  The data logger will fall by means of a parachute along with the other whirly birds at a descent rate similar to or the same as the whirly birds.  This way, data can be gathered from the displacement of the whirly birds and atmospheric data can be determined from the data logger.  The mission success criteria for this payload is to recover the logger, download and view the data from the electronic device.  Information from the data logger could then be used for further missions to conduct comparative analysis.

The main variable is this experiment is precisely what is being tested, the wind.  High wind conditions should result in the whirly birds being carried substantially downrange, therefore providing a wide splatter gram.  Moderate winds will allow for simple recovery of all the pods and a smaller dispersion, whereas low wind conditions will yield less useful results, as the whirly birds will simply land near the launch pad.  Toto, the electronic data logger, will allow for low altitude study of temperature and relative humidity.  Controls for the experiment will include a weather station set up at ground level that will monitor the surface level winds, temperature, and relative humidity.  All devices will be in close proximity to each other before launch to note any difference in base level readings.  The actual readings may not necessarily be used for analysis; rather the changes over time may prove to be more important.

Hypothesis: 	Ground level wind speed is the same from ground level up to 5280 feet above ground level.

Prediction:	Whirly birds dropped from the release point will land within a specific location based on calculations if the wind velocity remains constant during free fall.

Assumptions:	The whirly birds will reach terminal velocity immediately upon ejection from the payload section of the launch vehicle, thus resulting in the elimination of gravity into the equations.

The main variable for this launch is the wind.

Relevance of expected data, accuracy / error analysis:

Flight predictions for the whirly birds are based on the velocity of the winds at approximately 800 feet when the main parachute and payload will be deployed.  Any wind will cause the whirly bird to fly in a trajectory that is not totally vertical, therefore including a horizontal vector.  Establishing this vector using physics equations will allow for comparison to the surface level winds.  It is expected that the whirly birds will travel farther than the prediction based on the surface level wind speeds.  This hypothesis is based on real life occurrences experiences during the Team America Rocketry Challenge finals held in Manassas, Virginia.  The team noticed that the weather balloon station set up on site seemed to always indicate that the wind speed was progressively higher at each successive altitude marker.  To complete the mission, the team is attempting to derive a linear equation that can predict the wind speed at certain altitudes in order to conclude where biological spores could land if released from known altitudes.  Preliminary study was to release whirly birds at apogee and 800 feet.  Having two data gathering points would have allowed for better error analysis to improve the accuracy of the prediction equation.  However, having only one data set from the April, 2008 launch will limit the accuracy values.  Therefore, the Cougar Rocketry Team is going to attempt to compare the data with the April launch to the proposed test flight to be held in February or March of 2008. Low altitude tests with the 66% scale rocket will also be conducted in order to establish a baseline for ejections at 800 feet if the scale version is capable of attaining this altitude.

The data ball, Toto will collect atmospheric data at a proposed rate of one unit per second.  This data rate is established by the manufacture of the devices.  Currently, this data rate is believed to be too slow establish useful information, however, the team plans to keep this payload in place in order to learn more about electronic data gathering.

Refer to Flight Performance Predictions and Possible Graphical Scenarios to view estimated plots and data.

Experiment Process Procedures:

A series of events must occur in order to maximize the potential for success of the payload.

- All Whirly Birds are to be the same size and approximate mass

- Whirly Birds must be free to release from the airframe without restriction

- Ejection charge must be of sufficient strength to eject entire payload

- Whirly Birds must not become entangled in recovery systems

- Whirly Birds must be physically located for GPS data acquisition

- 75% of the Whirly Birds must be located for reliable results

- Whirly Birds must not be damaged at any time during the flight or descent to Earth

- Data must exhibit a positive or negative mathematical correlation to formulate equation

- Electronic Data Ball “Toto” must sustain the excessive launch forces

- Parachutes must not be damaged upon ejection (burnt or torn)

- Toto must have the same descent rate as the Whirly Birds

- Toto must land in a location capable of retrieval

- Electronic data storage devices must operate correctly to retrieve vital data from flight

- Computer analysis of data should agree with the Whirly Bird data

- An attempt of transmitting real time data during flight is in process

Experiment Design of Payload

Because the whirly birds are not electronically controlled, they require no calibration prior to launch. Since each whirly bird is made by hand, there is an uncertainty in the folding of each individual piece. It is therefore possible that each whirly bird may deviate slightly from others regarding flight characteristics. These deviations are not considered significant because the dispersion of the whirly bird group is expected to cover a radius of approximately 200 yards down to 50 yards based on the significance of the wind velocity.   At the current time, weather conditions have severely hampered any continued measurements for the whirly bird velocity testing.  Once acceptable conditions are available, further testing will be conducted to measure the repeatability of the payload.  Once a determination of descent rate for the whirly birds has been made, the data logger will then be sized with an appropriate parachute to sustain the same descent rate.

The Yough Cougar Rocketry team believes that Dorothy II’s design is highly aerodynamic and well balanced in proportion.  It is believed that this design in Dorothy II will ensure a successful mission when the Range Safety Officer ignites her in Huntsville, Alabama.

Preliminary analysis of the descent rate of the whirly bird will be determined using a grid sheet marked in feet and inches. A team member will then videotape a whirly bird as it is dropped to measure time and displacement.

The equation and solving for the acceleration yielded .  As the whirly bird dropped, its path could be seen on the video and the time was measured from the camera counter.  This process is the same as is used in the Discovery Channel television show, Mythbusters.

A similar test to find the acceleration of the whirly bird was done by placing a whirly bird inside of the ¼ scale launch vehicle and a paintball without any crepe paper attached.  The rocket was launched and videotaped.  Once again, the camera timer was used to determine the time for the equations.  From the video, the rocket reached apogee at 64 feet.  The paintball can be heard impacting the football field.  The difference in time was 2 seconds, yielding the 64-foot altitude at ejection using  and 32 feet per second squared as the acceleration of gravity.  The whirly bird landed 10 seconds after ejection.  Using   and the 64 feet as the vertical displacement, the acceleration of the whirly bird was found to be 1.28 feet per second squared.  Due to the amount of streamer material for each whirly bird, it has been determined that the payload will reach terminal velocity almost immediately upon ejection.  Therefore, the acceleration of the whirly bird can be considered constant throughout the flight path.

The integrity of the design is solid. During a test of the whirly bird being ejected from a rocket, it was noted that some of the crepe paper became scorched.  It is believed that this may decrease the amount of drag on the whirly bird in flight, but to what extent, the team has been unable to measure since the amount of burnt crepe paper cannot be predicted.  Therefore, it is the goal to provide a flame free environment for the whirly bird at all times to eliminate the scorching effect.  The electronic data logger, Toto, will download information regarding temperature and relative humidity during it descent.

The whirly birds design causes it to open its wings when it is ejected out of the rocket therefore the wings of the whirly bird become untwined and spin like a helicopters blade causing it to flutter down to the ground safely.

Our workmanship in the creation of the whirly birds is to ensure that the whirly birds are cut to the same length, weigh the same, and consist of the same material.  The electronic whirly birds will be made to fall at the same descent rate as that of the whirly birds.

Flight Performance Predictions and Possible Graphical Scenarios

Flight Performance Predictions and Possible Graphical Scenarios

Flight Performance Predictions and Possible Graphical Scenarios

The scientific hypothesis of our experiment is to determine if the surface level winds are an accurate predictor of wind speed at an altitude of 5,280 feet (1 mile). Using the topographical map and GPS locations, the horizontal distance can be determined. Physics equations can then be utilized to calculate the average wind speed experienced by the whirly bird. These values can then be compared to the predicted values before launch. Statistical calculations will then be compared to determine if there is sufficient evidence to support or refute the hypothesis.

In order to find the time of the drop for the whirly birds, the altitude at ejection will be retrieved from the altimeter.  This value will then be used to calculate the time using distance = rate * time.  Making the assumption that the payload will be ejected at 5280 feet and 800 feet, the time to reach the ground on a perfectly still day would be 637 seconds and 96 seconds respectively using the descent rate at a constant 8.28 feet per second.  To calculate the horizontal displacement, the use of d = rt is once again utilized.  This time, the rate will be the wind speed measured in MPH then converted to feet / sec for calculations.  The table shows estimated displacements from the launch pad based on varying speeds of the ground level winds.

If the calculated distance differs from the actual distance to the landing of the whirly birds, then the above situations will be examined to determine which is the most feasible for analysis.  Once all data is collected, then the process of interpreting the data can be completed for final analysis and interpretation.

Estimated Displacement from Launch pad of Whirly Birds

| Wind | Wind | Estimated Horizontal Displacement from Apogee | Estimated Horizontal Displacement from Main Chute Ejection |
| --- | --- | --- | --- |
| MPH | Feet / sec | Feet | Feet |
| 0.5 | 0.733 | 467.13 | 70.40 |
| 1.0 | 1.467 | 934.27 | 140.80 |
| 1.5 | 2.200 | 1401.40 | 211.20 |
| 2.0 | 2.933 | 1868.53 | 281.60 |
| 2.5 | 3.667 | 2335.67 | 352.00 |
| 3.0 | 4.400 | 2802.80 | 422.40 |
| 3.5 | 5.133 | 3269.93 | 492.80 |
| 4.0 | 5.867 | 3737.07 | 563.20 |
| 4.5 | 6.600 | 4204.20 | 633.60 |
| 5.0 | 7.333 | 4671.33 | 704.00 |
| 5.5 | 8.067 | 5138.47 | 774.40 |
| 6.0 | 8.800 | 5605.60 | 844.80 |
| 6.5 | 9.533 | 6072.73 | 915.20 |
| 7.0 | 10.267 | 6539.87 | 985.60 |
| 7.5 | 11.000 | 7007.00 | 1056.00 |
| 8.0 | 11.733 | 7474.13 | 1126.40 |
| 8.5 | 12.467 | 7941.27 | 1196.80 |
| 9.0 | 13.200 | 8408.40 | 1267.20 |
| 9.5 | 13.933 | 8875.53 | 1337.60 |
| 10.0 | 14.667 | 9342.67 | 1408.00 |
| 10.5 | 15.400 | 9809.80 | 1478.40 |
| 11.0 | 16.133 | 10276.93 | 1548.80 |
| 11.5 | 16.867 | 10744.07 | 1619.20 |
| 12.0 | 17.600 | 11211.20 | 1689.60 |
| 12.5 | 18.333 | 11678.33 | 1760.00 |
| 13.0 | 19.067 | 12145.47 | 1830.40 |
| 13.5 | 19.800 | 12612.60 | 1900.80 |
| 14.0 | 20.533 | 13079.73 | 1971.20 |
| 14.5 | 21.267 | 13546.87 | 2041.60 |
| 15.0 | 22.000 | 14014.00 | 2112.00 |

The team’s integration plan includes the following known details:

1.	Provide Mr. Eric Haberman with the G10 material to be cut for fins and beveled

2.	Begin construction of the electronics bay

3.	Assemble bulkheads to create electronics bay

4.	Install motor mount assemble provided by Mr. Eric Haberman

5.	Install and epoxy fins upon return from Mr. Walters

6.	Install hardware for attachment of shock cord and parachutes

7.	Attach launch rail buttons

8.	Mask off rail buttons and sand smooth the body tubes

9.	Apply primer and paint launch vehicle

10.	Apply decals

The Instrumentation used in Dorothy includes the G-Wiz LC 800 altimeter.  For the specifications about this device, please refer to the document LC800 in PDF format.

In order for the whirlybirds and Toto, the electronic whirlybird, to follow the mission goals, they need to flutter towards the ground with a similar decent rate. In order for them to perform this function, they are constructed to have the same length of crepe paper and have similar masses since paintballs of the same brand are to be used. Further testing with the decent rate of Toto is to take place to determine the proper parachute size to achieve a similar decent rate to those of the regular whirly birds. The picture below demonstrates how many of the whirly birds will flutter towards the ground after being deployed from Dorothy II upon reaching apogee.

Repeatability of instrumentation and measurement includes each length of crepe paper being precisely measured and each paintball being weighed in order to give them similar masses as well as similar decent rates.  The team tested the repeatability of the design criteria of the descent rates by dropping twenty whirly birds off of the bleachers of the high school stadium, which is ninety feet tall, and found that each whirly bird hit the ground within a time span of 3.28 seconds.  There is uncertainty as to the exact timing, due to the fact that the whirly birds timing was done with handheld stop watches.  The individual timing the whirly birds descent rate is not exact due to the fact that human reaction time is not always the same during each drop.  It was noted however, that the average time for the drops made was very close to the time that was measured by using the digital video camera and its timestamp.

The application of engineering for this project is to understand and create a man made synthetic device that can best recreate an object found in nature. Man has always tried to understand natural events and the creation of the whirly bird does such, the flight of a maple tree seed. The functionality of the whirly birds is to mimic the maple seedpods found in nature. The whirly birds feasibility indicate its realistic and simplistic ways for constructing each whirly bird and its ability to easily mimic the helicopter style of falling that maple tree seed pods.

Flight Preparations Procedures

All materials needed for the creation of the whirly birds will be reused from SLI 2007.  Some of the whirly birds were damaged last year, many are still able to be used.  Paintballs were purchased from Wal-Mart and additional crepe paper was acquired at a local party store.  The procedures required for proper payload deployment are to load the whirly birds into the sabot with the paintball in the aft end of the sabot.  This location minimizes shifting during thrust.  The electronic data logger will be the first item into the ejection sabot, followed by the whirly birds, then the SkyAngle CERT-3 parachute.

Mission success depends on each component working as designed and tested.  The SkyAngle CERT-3 parachute has shown it’s proven reliability for much high power launches.  There are no testing procedures that can be conducted by the team.  A visual inspection will be made to ensure there are no tears in the material or shroud lines.  Safe descent relies on this component, which is why it is the first to eject from the airframe.  In order to yield accurate results for the whirly birds, each one must be created in the same manner and have the same mass.  Attempts to measure the mass of 100 whirly birds proved to be tenuous.  The digital scale being used did not even show a difference from object to object.  Toto’s mission will depend on the sensitivity of the data logger.  Even the company that provided the logger, General Tool, is unsure as to the reaction time of the logger during its descent.  General Tool is awaiting the teams findings in order to analyze the data an possibly make revisions for further products.

Assembly

Whirly Bird Payload Assembly

| Assembly Step | Assembly Personnel | Assembly Verification |
| --- | --- | --- |
| Unpack paintballs from container and count out 100 paintballs | Ashley Wiley | Amy Bickerstaff |
| Cut streamer material into six foot lengths | Ashley Wiley | Stephanie Abbott |
| Place paintball into the center of streamer; fold over and tape into place | Ashley Wiley | Amy Bickerstaff |
| Neatly roll up streamer material for compact fit into the sabot | Ashley Wiley | Stephanie Abbott |
| Place whirly birds into the sabot in an organized and neat fashion | Ashley Wiley | Josh Sarosinski |
| Place sabot carefully into the launch vehicle | Ashley Wiley | Eric Haberman Josh Sarosinski |

The variables for this experiment are time, wind speed, altitude of launch vehicle, and wind direction. The constants will be gravitational acceleration, mass of the whirly birds, and the coefficient of drag encountered by the whirly bird.

The experiment process procedures include:

Whirly birds

  - Purchase a container of paintballs

  - Separate 100 paintballs

  - Cut forty inches segments of crepe paper

  - Place one paintball in the center of each piece of crepe paper

  - Secure paintball using a rubber band and/or tape to create a whirly bird

  - Fold and roll crepe paper to within three inches of paintball

  - Secure whirly bird into a storage container

  - Remove whirly birds from storage container and pack into the sabot

  - Insert sabot into payload section of launch vehicle

  - Payload is now ready for deployment

Toto

  - Remove electronic whirly bird (a.k.a. Toto) from it package

  - Install batteries into electronic whirly bird

  - Connect laptop to electronic whirly bird

  - Enable start time and sample rate for electronic whirly bird

  - Verify clock setting for electronic whirly bird

  - Disconnect laptop from electronic whirly bird

  - Attach parachute to electronic whirly bird

  - Insert electronic whirly bird into sabot with crepe paper whirly birds

  - Payload is now ready for deployment

Safety and Environment ( Payload )

Stephanie Abbott is the Safety Officer for the Yough Cougar Rocketry Team.

Failure of the following launch vehicle items must be addressed to ensure proper ejection and recovery of the payload incased in Dorothy II.

Fins: In the event that a rocket fin would fall off, then the rocket could possibly fly uncontrollably in any direction causing the payload to be damaged or inaccurately released at an altitude not suitable for data analysis.  To prevent such an event, ensure that the fins are properly epoxied into the airframe and that the fin material is of appropriate strength to withstand the forces encountered.

Motor and Parachute- In the event that the motor doesn’t fire properly,

- If the motor does not have enough thrust then the rocket might not reach its potential apogee, thus causing the chalk demonstration to yield unsatisfactory results.

- Rocket could yaw excessively under low or partial thrust causing the payload to be damaged or be destroyed during a high-speed ground impact.

- If the parachute deployment is altered by motor malfunction, the parachute may not deploy; therefore resulting in the payload failing to deploy from the airframe.

Sabot and Whirly Birds - in the event of the sabot malfunctioning

- The payload might not come out causing the parachute to malfunction and not deploy

- The whirly birds might tangle up in the sabot causing the sabot to lock up and fail to release the whirly birds

- Sabot may lock up inside of the airframe, causing the whirly birds

Personal Hazards and Avoidance Procedures

Cuts from sharp instruments, scissors: don’t run with scissors

Burns from soldering iron: place soldering iron in holder when not in use

Poison risk from paintballs: do not ingest or apply pressure to paintball causing rupture

Static discharge cautions: properly ground oneself before handling electronic devices in data ball

Other First Aid: Locate first aid kit in a location convenient to all personnel in the working environment in case injury occurs

Additional personal hazards that can occur include,

Before the rocket launches

- Failure to arm the ejection charge systems resulting in payload not being deployed

- Accidental launch before spectators are at a safe distance causing payload to land in the spectator area

- Personnel could drop or damage rocket causing system failures

To prevent such things from happening

- Have more than one person overlooking preparation of launching and ejection systems

- Make sure that everyone is in the safety zone before launch of the rocket

- All personnel need to be aware of the surroundings to watch for falling payload items

- Store rocket in a secure location to prevent damage to the payload

During the rocket launch

1.) Personnel could lose visual contact with the launch vehicle and payload

2.) Rocket could have a malfunction resulting in payload impacting nearby equipment or

personnel

To prevent such things from happening

- Have more than one person watching the payload and pin-pointing a location for landing

- Watch the payload at all times and if payload approaches, seek cover

- Monitor the location of all payload pieces in order to recover and pick up to prevent environmental harm

Environmental Concerns

If the payload is not recovered

- Animals may attempt to ingest crepe paper or paintballs, therefore becoming sick

- Battery from Toto could leak into the Earth and cause contamination of the nearby soil and/or groundwater supply

- Electronic boards in Toto could deteriorate if left in an outdoor environment for a prolonged time period, thus resulting in possible contamination of the nearby soil and/or groundwater supply

- Plastic encasement for Toto could separate and leave behind sharp plastic material capable of injuring an individual or animal if stepped upon

Things to do to prevent such things from happening

Many of the materials used in the construction of Dorothy II are made of biodegradable substances and designated personnel are to monitor any pieces that may detach from the airframe.

Ensure that regulations and procedures required by the NAR are observed at all times.  Instructions for all internal devices and deployment systems are to be kept in a binder as well as any MSDS sheets for materials being handled.

# Payload

The whirly birds are constructed of crepe paper and paint balls, both of which are biodegradable.  These pose little to no risk to the environment.  The data logger is constructed of hard plastic and includes a lithium battery.  Recovery of this device is essential to mitigate environmental situations.  A designated spotter will track this device specifically.  A parachute of a high contrast color will be attached to this device so that it is easy to spot both in the air as well as on the ground.

V). 	Launch Operation Procedures

Checklist – Launch Vehicle Preparation and Assembly

| Assembly Step | Assembly Personnel | Assembly Verification |
| --- | --- | --- |
| Assemble Animal Motor Works L900RR | Joe Paskolka | Amy Bickerstaff |
| Install L900RR into launch vehicle airframe | Joe Paskolka | Amy Bickerstaff |
| Secure L900RR using latching system | Joe Paskolka | Amy Bickerstaff Donald L. Gilbert, Jr. |
| Verify battery levels | Josh Sarosinski | Eric Haberman Donald L. Gilbert, Jr. |
| Check that all wiring is secure and undamaged | Josh Sarosinski | Joe Paskolka Eric Haberman |
| Verify the systems are UNARMED | Stephanie Abbott | Joe Paskolka |
| Assemble ejection charge packets ( High Risk – Use Extreme Caution ) | Joe Paskolka Eric Haberman | Ashley Wiley |
| Place ejection charges into launch vehicle | Joe Paskolka | Ashley Wiley |
| Run wiring through launch vehicle to electronics bay | Stephanie Abbott | Joe Paskolka Eric Haberman |
| Verify the ejection systems are UNARMED | Stephanie Abbott | Joe Paskolka Eric Haberman |
| Connect ejection charge wiring to altimeter ejection charge connections | Josh Sarosinski | Joe Paskolka |
| Insert batteries into holders of the electronics bay | Josh Sarosinski | Eric Haberman |
| Verify all connections | Amy Bickerstaff | Joe Paskolka Eric Haberman |
| Signal the “ALL CLEAR” | Ashley Wiley Amy Bickerstaff | Range Safety Officer |
| Arm ejection systems to verify continuity of systems via LED lights | Amy Bickerstaff Joe Paskolka | Eric Haberman Donald L. Gilbert, Jr. |
| DISARM ejection systems | Amy Bickerstaff | Joe Paskolka |
| Verify all connections before inserting payload pouches | Ashley Wiley | Joe Paskolka |

Final Assembly

| Assembly Step | Assembly Personnel | Assembly Verification |
| --- | --- | --- |
| Attach payload pouches to shock cords | Ashley Wiley Amy Bickerstaff | Stephanie Abbott |
| Insert payload pouches into the launch vehicle airframe | Amy Bickerstaff | Ashley Wiley Earnest Walters |
| Verify that payload does not interfere with the ejection charge wiring | Ashley Wiley | Joe Paskolka |
| Insert electronics bay ( tube coupler ) into lower main body of launch vehicle using QuickLinks | Josh Sarosinski Stephanie Abbott | Earnest Walters |
| Insert nose cone into upper payload section of the launch vehicle airframe using QuickLinks | Amy Bickerstaff | Earnest Walters |
| Check for any binding of the nose cone or tube coupler that would prevent separation | Ashley Wiley | Josh Sarosinski Earnest Walters |
| Perform continuity check of igniter | Josh Sarosinski | Earnest Walters |
| Insert igniter into L900RR motor | Joe Paskolka | Range Safety Officer |

Final Assembly Continued

| Slide launch vehicle onto launch rail | Amy Bickerstaff Donald L. Gilbert, Jr. | Earnest Walters Range Safety Officer |
| --- | --- | --- |
| General inspection of launch vehicle | Amy Bickerstaff Ashley Wiley Stephanie Abbott Josh Sarosinksi | Earnest Walters Joe Paskolka Eric Haberman Donald L. Gilbert, Jr. Range Safety Officer |
| Obtain permission to connect igniter | Donald L. Gilbert, Jr. | Earnest Walters |
| Verify all spectators are clear of the launch pad and are at a safe distance | Amy Bickerstaff Ashley Wiley | Stephanie Abbott |
| Connect igniter to launch system | Earnest Walters Josh Sarosinski | Donald L. Gilbert, Jr. Range Safety Officer |
| Obtain permission for launch | Donald L. Gilbert, Jr. | Earnest Walters |
| Signal the intention to launch | Donald L. Gilbert, Jr. Amy Bickerstaff | Earnest Walters |
| Verify all spectators are aware of launch countdown | Amy Bickerstaff Stephanie Abbott | Ashley Wiley Range Safety Officer |
| Continue countdown | Ashley Wiley | Eric Haberman |
| LAUNCH | Name drawn from hat | Range Safety Officer |

Recovery Operations

| Recovery Step | Recovery Personnel | Recovery Verification |
| --- | --- | --- |
| Track flight path of launch vehicle to apogee and ejection | All Team members | All Team members |
| Track whirly bird payload to ground | Amy Bickerstaff | Ashley Wiley |
| Track Toto to the ground | Stephanie Abbott | Josh Sarosinski |
| Track flight path of launch vehicle to landing | Donald L. Gilbert, Jr. | Joe Paskolka |
| Measure locations of whirly bird landing sites using GPS device | Amy Bickerstaff | Ashley Wiley Stephanie Abbott Josh Sarosinski |
| Recover launch vehicle | Donald L. Gilbert, Jr. | Earnest Walters |
| Recover any loose parts if necessary | Donald L. Gilbert, Jr. | Joe Paskolka |

# Post Flight Inspection

| While Recovering | Recovery Personnel | Recovery Verification |
| --- | --- | --- |
| Ensure that it is safe to approach Dorothy II | Stephanie Abbott Amy Bickerstaff | Ashley Wiley Donald L. Gilbert, Jr. |
| Ensure that all ejection charges were properly fired | Stephanie Abbott Amy Bickerstaff | Ashley Wiley Earnest Walters |
| Ensure that motor was properly fired | Stephanie Abbott Ashley Wiley | Amy Bickerstaff Earnest Walters |
| Ensure that sabot and whirly birds properly ejected | Josh Sarosinski | Eric Haberman Stephanie Abbott |
| Collect 75% of crepe paper whirly birds and collect electronic whirly bird | All Team Members | Donald L. Gilbert, Jr. Earnest Walters Eric Haberman |

# Post Flight Inspection Continued

| After Recovery | Recovery Personnel | Recovery Verification |
| --- | --- | --- |
| Recover any loose shrapnel | All Team Members | Donald L. Gilbert, Jr. |
| Safely contain and dispose of shrapnel | All Team Members | Eric Haberman |
| Scatter plot whirly bird data | All Team Members | Donald L. Gilbert, Jr. Eric Haberman Earnest Walters |
| Return Dorothy II to prep area | All Team Members | Donald L. Gilbert, Jr. Eric Haberman Earnest Walters |
| Remove motor from Dorothy II | Earnest Walters | Earnest Walters |
| Pack Dorothy II into containment unit | All Team Members | Donald L. Gilbert, Jr. Eric Haberman Earnest Walters |

# Safety and Quality Assurance

The risk of any payload particles falling down and making human is unlikely, but in the unfortunate event that a person would be in the proximity of a whirly bird, the lightweight design and low velocity should not result in any bodily damage. There might be a small chance of a paint ball bursting on impact, which would require washing the paint off thoroughly with soap and water. The attached cord that runs through the center of the payload should not break off and do any harm inflictions to the environment, but in case of a major mishap, yell “HEADS UP.”

To ensure the safety of all rocketeers, a checklist listed above has been issued. When handling any materials used to make the rocket dealing with the payload section, mentors have been issued to watch each process

General Launch Operations Procedures as per Tripoli Safety Code

Nose Cone, Couplers – Ensure proper fit of nose cone and payload couplers

Flight Check (Safety Officer)

The data below provides a list demonstrating that the risks are at acceptable levels.

Construction Check – Ensure that the launch vehicle is well constructed with no loose parts

Safety Officer may wish to question any part of the construction with team members

Certification – Check the credentials of the team to certify a level II or greater member

Flight Plan

Check that the motor has sufficient impulse for safe launch

Ensure flight will not exceed the waiver limits issued by the F.A.A.

Verify recovery devices are in place and have been tested

Check that cloud ceilings are above maximum altitude capabilities

Calculate for variation of drift due to wind

Check that the rocket is stable by the locations of the CG and CP

Motor Installation

Verify that the motor is securely mounted in the airframe

Check that the igniters are free from cracks or lack pyrogen tip

Avionics

Arm ejection charge on launch pad ONLY

Check continuity of igniter once all spectators are away from launch pad

Pad Check (RSO or Pad Manager)

Controller – Check and be sure that the rocket is disarmed before approaching launch pad

Launch Pad – Check for stability and adequate size for rocket to be flown

Ensure that spectators are at the minimum safe distance for motor impulse

Launch Rod or Guides – Check that rocket slides freely, clean if necessary

Igniter Clips – Check and clean the leads

Pre Launch Check (RSO)

Avionics – Armed and ready for launch

Look and Listen – Check for aircraft in the launch area.  Stop launch for incoming aircraft

Flight Witnesses and Spotters – Present and made aware prior to launch

Launch (LCO)

Announce Launch

Ensure all spectators are aware of the launch

Provide a LOUD countdown such as 5, 4, 3, 2, 1 … Fire!

Monitor Flight Path – Yell “HEADS UP” for any rocket approaching any area with spectators

Disarm controller, place cap on launch rod after launch

Misfire Procedures (LCO)

Wait a minimum of one minute before approaching launch pad

Disarm launch controller and avionics if present

Remove failed igniter and motor if necessary

Replace igniter and follow launch procedures

Before the rocket launches

  - Eliminate all possibilities by installing devices of importance incorrectly

  - Eliminate all possibilities to accidentally launch before everyone is safely behind safety shield or standing at a safe distance

  - Eliminate all possibilities to have anyone approach the rocket and cause injury to one’s self or the launch vehicle

To prevent such things from happening

- Have more than one person overlooking preparation of launch vehicle assembly

- Make sure that everyone is behind a safety shield or a safe distance from the launch pad as designated by the RSO before someone arms or launches the rocket

- Ensure that all personnel inside the launch area are aware of all activities and have necessary safety gear and emergency escape routes

- Have the launch vehicle in a secure area

During the rocket launch

1.	During the launch, the launch vehicle could be lost if no one is tracking its path visually from the ground.

2.	The launch vehicle could break apart or encounter an electronic malfunction resulting in catastrophic system failure causing multiple fiberglass fragments falling downward to the launch or spectator area.

To prevent such things from happening

- Have more than one person watching the rocket and pin-pointing a location for landing

- Watch the rocket at all times if debris falls from the launch vehicle.  The person identifying any debris is to track its path to the ground and recover once the RSO has designated the area safe

Environmental Concerns

If the rocket catches on fire then

- Wild-fire can occur if grass is dry enough

- Scorching of area around rocket can occur if the grass is damp

- Debris which is not recovered could be ingested by animals

- Debris which is not recovered could damage vehicles or machinery traveling through the area

- Debris which is not recovered could harm the local ecosystem

Things to do to prevent such things from happening

When possible, use biodegradable materials to reduce environmental harm and assign specific personnel to track debris if required.

To ensure that we are not taking any unnecessary risks Eric Haberman and/or Ernest Walters will be overseeing that we follow proper operations for each section of the checklist listed above.

VI).	Activity Plan

Budget Plan

Due to substantial changes in the budget for NASA, the Yough Cougar Rocketry Team has been asked to pay for the expenses incurred for the culminating activity for the NASA SLI 2008 to be held from April 23 – 28, 2008.  The team anticipated the $1250 grant monies would be used to purchase the Quest Starhawk rocketry kits to be used in the outreach.  Currently, that money is being reserved to assist with the transportation costs and lodging for the team.

Below is the proposed budget as outlined in the original proposal

Proposed Budget

The proposed budget for “The Whirly Bird Experience” will be an ongoing and updated element of the project.  As the design evolves, new materials will need to be added and some removed.

| Part Description | Manufacture or Supplier | Cost |
| --- | --- | --- |
| Nose Cone | Performance Rocketry | $ 30.00 each (2) |
| Body Tubes | Performance Rocketry | $ 18.00 per foot (16) |
| Tube Coupler | Performance Rocketry | $ 64.00 |
| MadDog Dual Deploy Kit | Performance Rocketry | $ 159.00 |
| Payload ( paintballs ) | Wal-Mart | $ 30.00 per 1000 |
| Parachute ( drogue ) | SkyAngle Cert – 3 | $26.13 |
| 3/16” G10 Fins | Performance Rocketry | $30 per sheet |
| Parachute ( main 60” ) | SkyAngle Cert – 3 | $ 132.05 |
| Insta-Cure CA Glue | BSI Adhesives | $ 3.99 each (4) |
| Slow Set Epoxy | BSI Adhesives | $ 7.99 each (2) |
| Steamer Material | Wal-Mart | $ 1.99 per roll (3) |
| Sandpaper Assortment | Wal-Mart | $ 6.99 |
| Space Cad Software | Rocket Motion | $ 54.95 |
| RockSIM Software | Apogee Components | $ 99.99 |
| Altimeter Alt15K/WD | Perfectflite | $ 69.95 |
| LCX Dual Event Alt. | G-Wiz | $ 99.95 (2) |
| Rail Guides | Giant Leap Rocketry | $ 3.29 / pair |
| JB Weld | Wal-Mart | $ 5.65 |
| Krylon Paints | Wal-Mart | $ 5.97 per can (3) |
| PC-7 epoxy | Lowe’s | $7.97 |
| Starhawk Rocket for Outreach | Quest Education | $95.00 per 25 rockets (8) |
| Motors for Outreach | Quest Education | $39.00 per 25 motors (8) |
| Estimated Total Cost of Launch Vehicle and Payload | $ 2365.69 |

The ¼ or 66% scale model will be built primarily with Estes products.  Some items are already available to the team with leftover parts from TARC.  Below is an estimate of costs for the scale model.

| Part Description | Manufacture or Supplier | Cost |
| --- | --- | --- |
| Nose Cone BT-80 | Estes | $ 7.99 |
| BT – 80 Body Tubes | Estes | $ 13.79 |
| BT – 80 tube couplers | Estes | $ 8.99 |
| Parachutes | Top Flite Recovery LLC | $ 12.99 |
| Insta-Cure CA Glue | BSI Adhesives | $ 3.99 each |
| Motor ( Aerotech F – 20 ) | Red Arrow Hobbies | $ 25.95 each – need 3 |
| Basswood Fin Material | Midwest ( Tower Hobbies ) | $ 2.85 per sheet – need 3 |
| Estimated Total Cost of Scale Launch Vehicle and Payload | $ 108.20 |

The total estimated cost of the materials for both launch vehicles is projected to be $ 2473.89.  This value would be under ideal circumstances.  Since we are constructing such a large-scale rocket and items may change, this budget is only an estimate as some of the materials purchased for the 2007 SLI could be reused.

Funding Sources

Upon acceptance of the proposal, the Yough Rocketry Team will use the funds provided by NASA through the SLI grant as well as outside resources.  The owner of BSI Adhesives, maker of the Quik – Set and Slow – Cure epoxy has already provided products from the company inventory. Westinghouse has already provided a $2000 gift after the 2006 – 2007 NASA SLI was completed in hopes that the funds would be used to reconstruct Dorothy for the 2007 – 2008 SLI.  This was due to the fact that Mr. Eric Haberman, an employee of Westinghouse, fabricated the fiberglass for the original Dorothy.  Mr. Haberman’s name, as well as Westinghouse, was mentioned in several local newspapers, thus showing the commitment to education from the Westinghouse Corporation.   Local businesses have allowed the team to place fundraising materials (lollipops, candy bars, and trail mix snacks) in their establishments to increase the funding availability.  These items provide an average of 90% profit on each item sold.  Individuals are also selling the fundraising items during school hours in room 100, the main office, and in the hallways.  Last year, these sales accounted for an income of approximately $1400, which supplemented the teams meals and souvenirs during the Huntsville trip.  Ashley Wiley’s mother, Donna Montecupo, also solicited funds from local businesses in excess of $300.  With the continued success of the Cougar Rocketry Team, more business establishments are becoming more willing to fund the team’s endeavors.  Some of these businesses have been increasing their donations each year as the Cougar Rocketry Team continues to grow.  State Representative Ted Harhai and Senator Bob Regola also plan to ask the Commonwealth of Pennsylvania for a grant designed specifically for rocketry based projects upon acceptance into the 2007 – 2008 SLI program.

A breakdown of additional expenses is provided below.

| Item Required | Cost each | Total Cost | Paid / Unpaid |
| --- | --- | --- | --- |
| Airline Tickets | $ 270 | $ 2,700 | Unpaid – $ 400 Deposit sent |
| Lodging | $ 75 per room per night + tax | $ 2125 | Unpaid |
| Meals | $ 40 per person per day | $ 2000 | Unpaid |
| Rental Van | $ 600 per week | $ 600 | Unpaid |
| Total Cost |  | $ 7425 |  |

At the time of the writing of this document, the computer sales have yielded a total income of $4140.  Approximately $2100 has been raised through candy sales thus far.  Other organizations have also been selling similar items, thus cutting into the sales volume once experienced by the teams’ sales.  The Pittsburgh Penguins, Steelers, and Pirates have been donated some items for a Chinese Auction to be held in March or April.  Seven Springs Ski Resort also donated ski passes and tubing tickets.  Some restaurants and stores are also donating gift cards.  The team hoped to earn approximately $2000 from this event, however, the sales from the tickets have resulted in only an income of $800.

Timeline

The Cougar Rocketry Team plans to use the following timeline for implementation of the mission goals for Project Dorothy.

September 2007;

- 20th – Have the proposal completed in rough draft form

- 24th – Have the proposal in completed form

- 27th – Mail proposal, no later than, September 29th

- 29th – Send e-mail as backup copy

All September Mission Goals Complete

October 2007:

- 1st     – NASA SLI Proposal received at Marshall Space Flight Center, Huntsville, AL

- 22nd – Await notification of selection

- 22nd – Submit Payment Information Forms

- 23rd – Arrange SLI Team Teleconference/ Video Teleconference

- 25th – Contact News agencies for coverage on the acceptance into the SLI program

- 26th – No School, Teacher in-service day

- 29th – Begin writing the Preliminary Design Review (PDR)

- 30th – Reconstruct the quarter scale rocket

- 30th – Update Website with current information and team data

- 30th – NASA media announces new 2007 – 2008 SLI Teams

- 31st – Halloween

All October Mission Goals Complete

November 2007

- 5th   – Web Presence Established (complete)

- 7th   – Launch of ¼ scale rocket (delayed due to poor weather conditions)

- 12th – No School, Teacher in-service day (complete)

- 13th – Launch of whirly birds to monitor flight characteristics (complete)

- 16th – Have PDR rough draft completed (complete)

- 22nd – Thanksgiving Day (we ate too much)

- 23rd – No School, Holiday Break (shopping was fun)

- 26th – No School, First Day of Deer Season (no animals were harmed by our team)

- 28th – Have PDR final copy completed

- 28th – Submit PDR to Julie Clift and post on Website

All November Mission Goals Completed

December 2007:

- 3rd    – Begin construction of full scale launch vehicle – Dorothy II

- 21st – Construction of Dorothy II complete in unpainted form

- 21st – Last Day of Classes before Christmas Break

- 25th – Christmas Day

- 27th – Team meeting to begin paint preparation

- 31st – New Year’s Eve

Construction of Dorothy II is behind schedule

January 2008:

- 1st    – New Year’s Day

- 2nd  – Classes resume

- 11th – Begin to finalize the Critical Design Review (CDR) and PowerPoint Slides

- 18th – Have CDR Presentation Slides and CDR report completed

- 21st – No School, Teacher in-service day (work day for team on CDR)

- 22nd – Critical Design Review submitted to Julie Clift and posted on Website

- 28th – Critical Design Review Video Teleconference

- 28th – Submit Second Invoice

All January Mission Goals Completed

February 2008:

- 2nd – Chinese Auction and Outreach at Sam’s Club Greensburg

- 4th   – Begin the Flight Readiness Review (FRR) Report

- 19th – Chinese Auction and Outreach at Giant Eagle, West Newton

- 14th – Valentine’s Day

- 18th – No School, teacher in-service day

- 19th – Rough draft of FRR complete

- 20th – Being the PowerPoint slides for the FRR

- 23rd – Possible test flight of Dorothy II at the Tripoli launch site ( launch was cancelled)

February Mission Goals Completed with the exception of test launch

March 2008:

- 10th – No School, teacher in-service day

- 14th – Have the FRR in completed form, both report and PowerPoint

- 17th – St. Patrick’s Day

- 19th – Lama’s Club Outreach

- 20th – No School, Easter Break begins – meeting to review FRR

- 23rd – Easter Day

- 24th – Flight Readiness Review submitted to Julie Clift and posted on Website

- 24th – Last day of Easter Break

- 31st – Submit the Flight Readiness Review invoice

April 2008:

- 1st – FRR presentation to NASA

- 2nd  – Paint completed on Dorothy II - delayed

- 7th   – Finalized test firings of ejection charge systems

- 15th – Begin the shipping procedures for the full scale rocket

- 21st – Dorothy II arrives in Huntsville via FedEX ground

- 23rd – Team travels to Huntsville, AL

- 24th – Rocket Fair

- 25th – Yough High School Prom

- 26th – Launch Day

- 27th – Travel back to Pennsylvania

May 2008:

- 5th   – Post – Launch Assessment Review (PLAR) in rough form

- 17th – Team America Rocketry Challenge

- 20th – No School, Snow makeup day

- 23rd – Post – Launch Assessment Review (PLAR) due

- 23rd – Submit final invoice for 2007 – 2008 SLI program

- 26th – Memorial Day, No School

Outreach – Business Involvement and Public Exposure

The YHS Rocketry Team will solicit donations from local businesses in exchange for advertising on the SLI web site.  High power rocketry skills will be acquired from the Pittsburgh Space Command rocketry club and Pittsburgh TRIPOLI chapter.  At least one member of the YHS Team will attend launches in the local area when possible.  Supplies will be sourced from various Internet locations and / or local NAR members.  The local UPS and FedEX shipping warehouse will be contacted to inquire about low cost or free shipping of the ground support and launch vehicle as necessary. WPXI television has already featured the YHS Rocketry Team in an earlier segment for TARC and as time permits for additional follow-up, will continue to monitor the progress of the SLI objective.  KDKA television has also shown an interest in the NASA SLI program; however, breaking news events have prevented news crews from visiting the Yough School District when the students were available.  The Greensburg Tribune-Review ran a feature article about the Cougar Rocketry Team and their accomplishments in April of 2007.  This article provided the much needed exposure to the program.  Editors at the newspaper informed the team that continued coverage would be available.  A reporter from the Pittsburgh Post-Gazette interviewed the team and will be featuring the team in the “local” section of the newspaper.  The Times Sun will once again speak to the team and advertise the rocket fair to be held at the high school on March 29, 2008.

Westinghouse Corporation’s Plasma Research Center located in Madison, Pennsylvania provided the Cougar Rocketry Team with a $2000 cash grant at the completion of the 2007 SLI after learning of the crash landing sustained by Dorothy.  Westinghouse has been an increasing presence in the community with regard to engineering projects, which are being completed in the Yough School District.  It was the intent of the Westinghouse Corporation to assist the team in successfully completing the mission first set forth by Dorothy I in 2007.  Mr. Eric Haberman, an employee of Westinghouse was vital in the construction role and fiberglass cutting for the original Dorothy.  His presence in the project was held in high regard within the Westinghouse community.  As repayment for the assistance of Westinghouse, the team visited the Waltz Mill plant during Engineering Week as student representatives from Yough School District.  Dorothy I and II were on display as well as the payload for the engineers to examine and ask questions.  Response to this event was very positive.

On March 19, 2008, the Cougar Rocketry Team presented a program to the Latrobe Llama’s club, an affiliate of the Freemason’s.  Members Amy Bickerstaff, Ashley Wiley, Stephanie Abbott, and Josh Sarosinski explained the Team America Rocketry Challenge and NASA SLI to approximately 60 individuals.  Chinese auction sales were able to supplement the team with another $120 including a $50 donation from the Llama’s organization.  Many of the Llama’s members are retired and were very much interested in the accomplishments of the team since they could recall where they were when Sputnik made its initial flight around the earth.

|  | The team members of Alicia Bowser, Amy Bickerstaff, Stephanie Abbott, Josh Sarosinski, along with Donald L. Gilbert, Jr., were greeted Westinghouse representative Kathy Slicz during Engineer’s Week. |
| --- | --- |
| Student Launch Initiative Members Alicia Bowser and Amy Bickerstaff discuss the NASA project with engineers at the Westinghouse Waltz Mill facility located in Madison, Pennsylvania. |  |  |

|  | Stephanie Abbott and Josh Sarosinski take their turn in explaining the various components and systems that make up Dorothy II as her older sister Dorothy I sits in the background. |  |
| --- | --- | --- |
| Mr. Eric Haberman, Westinghouse employee and mentor for the Yough Cougar Rocketry Team provides a tour of the Waltz Mill Facility including the training bays where technicians around the world come to learn how to service nuclear reactors for power generation. |

|  | The Yough Cougar Rocketry Team gathers around Dorothy I, the NASA SLI 2007 launch vehicle, on display with Mr. Eric Haberman. Completion of Dorothy I and II would not have been possible without the assistance of Mr. Haberman or the cooperation of Westinghouse Plasma Corp. |
| --- | --- |

The team has also been refurbishing computers that were once used in the labs of the schools to provide a service to the community.  These used computers are being sold to students and parents who are unable to afford new computer systems.  Some benefits of these sales are that old computers are not being thrown into the trash and damaging the environment as well as spreading the Cougar Rocketry Team name for beneficially serving the Yough community.  All of the computers were donated to the team by the Yough School District, therefore allowing all proceeds to go directly to the cost of the Huntsville trip in April.

A Chinese Auction has been held in conjunction with the new outreach program.  Items donated will be drawn for from tickets sold for $1, 3 for $2, 7 for $4, 20 for $10.  Minor costs are associated with this event and has earned over $800 thus far.

Outreach – Younger Student Involvement and Program being sustained

The student outreach has been highly modified due to the funding issues and restrictions placed on the team by the Yough School District.  The team is unable to conduct an outreach in the middle school science classes as once anticipated.  A new program has been devised to consist of distribution of the Quest Starhawk rocket during the public sales events for the Chinese Auction.  Seventy-five (75)  Starhawk rocket kits were distributed to children and young teens at the Greensburg Sam’s Club, and West Newton Giant Eagle.  Patrons were given a pamphlet including the Cougar Rocketry Team’s website to learn details of a rocket fair to be held at the high school on March 29, 2008.  Those who received and built their Starhawk will be given the opportunity to fly their rocket on a Quest A6-3 or Estes A8-3 motor.  The winners of the Chinese Auction will also be determined that day.

| Example of the rocket kit being built by the students for outreach |  |
| --- | --- |

VII).	Conclusion

The Yough Cougar Rocketry Team is very pleased to have been selected for the 2007 – 2008 Student Launch Initiative as a returning team.  Having completed the criteria during the 2006 – 2007 SLI, the group believes that they have achieved a higher level of understanding of the design process and implementation of a schedule plan.  The lessons learned last year after the disastrous fall of Dorothy has allowed the team to make modifications to the new design in order to possibly eliminate the failure of the recovery systems.  Even though Dorothy II is the same with regard to physical dimensions, the internal workings are totally new.  Dorothy II will even have a new look, sporting a new Wizard of Oz theme.  One of the benefits of the SLI program that the group is looking forward to is reacquainting with old friends from the previous year and meeting new ones this year.  Another goal the team wishes to achieve is to broaden the public eye as to the program and the accomplishments that are being completed within the Yough School District as the other sports overshadow the importance of the SLI program and sport rocketry.  From all of us, to all of you, thank you for another wonderful opportunity.